## Slide 1: Chapter 3
Process and Process Variables

## Slide 2: Process Diagrams and Variables
Diagrams are used to describe a process or set of processes
  The diagrams incorporate simple boxes for individual unit operations and lines for input and output streams
Unit Operation
(Process Unit)
Input
(Feed)
Output
(Product)

## Slide 3: Section 3.1—Mass and Volume
Density is one of the more important conversion factors because it allows direct conversion between mass and volume
  Abbreviated with 
Specific gravity is related to density by the use of a reference material’s density:
  Most common reference is water, which has a density of 1 g/cm3, 1000 kg/m3, and 62.43 lbm/ft3
  Specific gravity is unitless (a ratio of densities)

## Slide 4: Sample Density Problem
Calculate the density of mercury in lbm/ft3 using the tabulated specific gravity (13.546).
Calculate the volume in ft3 occupied by 215 kg of mercury.
Example 3.1-1 (pg. 44)

## Slide 5: Section 3.2—Flow Rate
Very few industrial processes operate as a batch process
  Most occur as a fluid flows in and out of a unit operation (distillation, reactor, heat exchanger, etc.)
Therefore it is more convenient to describe these processes using flow rates
  Either mass (mass/time) or volumetric (volume/time) flow rates
  Flow rates are distinguished from stationary amounts by the use of a dot:
    Ex: m vs. ṁ for mass vs. mass flow rate

## Slide 6: Density and Flow Rates
Density can be used with flow rates in the same manner that it can be used with stationary masses or volumes:

## Slide 7: Section 3.3—Chemical Composition
Molecular weight
  Expressed in various units in this course:
    g/mol, kg/kmol, lbm/lb-mol
      Ex: Molar mass of water is 18.02 g/mol or 18.02 kg/kmol or 18.02 lbm/lb-mol
    lbm/lb-mol = super confusing

## Slide 8: Mass and Mole Fractions
Mass fraction
Mole fraction
Notice that mole fraction is expressed with a y in this system and not the  you may be used to from AP Chem.

## Slide 9: Pressure
Pressure = Force/Unit Area
  Liquid pressure is directly related to density:
  P = gh
Frames of reference for pressure:
  Absolute pressure
    Relative to a vacuum
  Gauge pressure
    Typically relative to atmospheric pressure
Pabs = Pgauge + Patm

## Slide 10: Pressure Measurement
Most common instrument is a Bourdon gauge
  Wide range of uses (very low to very high pressures)
Manometers provide more accurate measurements for P < 3 atm

## Slide 11: Types of Manometers
Open-end
  Usually open to the atmosphere
Differential
  Measures a pressure drop between two points in the line
Sealed-end
  One end sealed such that a near vacuum is created (P  0)

## Slide 12: Manometer Equations
General Manometer Equation
Differential Manometer Equation
  1 = 2 ; therefore equation reduces to:
P1 – P2 = (f - )gh
Manometer Equation for Gases
  No liquids therefore pressure is simply related to the different fluid levels:
P1 – P2 = h

## Slide 13: Temperature and Temperature Scales
Temperature scales used or referenced:
  Celsius, Kelvin, Fahrenheit, Rankine
Conversions:
  T(K) = T(C) + 273.15
  T(R) = T(F) + 459.67
  T(R) = 1.8T(K)
  T(F) = 1.8T(C) + 32