## Slide 1: Chapter 7 Review
Things Covered Thus Far

## Slide 2: Closed System Energy Balances
No mass transferred across system boundaries
U + Ek + Ep = Q – W
U = 0 if process is isothermal
Ek = 0 if process is not accelerating
Ep = 0 if process is not changing height
Q = 0 if process is perfectly insulated (adiabatic)
W = 0 no energy transmitted across system boundaries

## Slide 3: Open System Energy Balances
Involves the flow of material into and out of the process being evaluated
H + Ek + Ep = Q – Ws
Terms cancel under the same conditions as before

## Slide 4: Additional Equations Related to Open System Energy Balances
The enthalpy term can be expressed as follows:
H = U + P V OR H = U + P V OR Ĥ = Û + PV
Specific enthalpy (Ĥ) can always be calculated using steam tables and therefore H or H can also be calculated:
H = mĤ OR H = nĤ
When dealing with the the P V term it is almost always necessary to convert using one or more of the gas constant, R, values listed in the back

## Slide 5: Important Questions Assigned Thus Far
From Chapter 7:
  1-3, 5, 9, 10, 12-13, 15-16, 19, 24, 25